## Slide 1: Development of a High-Energy Seed for Contrast Improvement of the Vulcan Laser Facility.
Ian Musgrave, W. Shaikh, M. Galimberti, A. Boyle, K Lancaster, C. Hernandez-Gomez, R. Heathcote.
Central Laser Facility, STFC,
Rutherford Appleton Laboratory, UK

## Slide 2
The Vulcan laser Facility
Nd Glass Laser
8 Beam CPA Laser
3 Target Areas
3 kJ Energy
1 PW Power

## Slide 3: Vulcan Petawatt
PC
F
Ti:S
BBO
BBO
BBO
Pump
Stretcher
F
F
Compressor
x3 208mm Nova disc amplifiers
16mm Phosphate rod
25mm phosphate rod
45mm Phosphate rod
Adaptive optic
Double pass 108mm phosphate disc
150mm disc
Beam diagnostics
Beam diagnostics+
wavefront sensor
Interaction
chamber
9mm silicate rod
Double pass 16mm silicate rod
F
Single stretch to 4.5ns
Combination of OPCPA and mixed glass amplifiers for amplification

## Slide 4: Existing PW facility ASE contrast
Previously used photo-diodes to investigate the ASE contrast of the Vulcan PW facility gave a baseline of ~108 for the ns ASE.
These have shown that the ASE is seeded by the pump pulse of the OPCPA, used NF apertures to limit fluorescence.

## Slide 5: Introduce High Energy Seed
Introduce a single stage of amplification before main stretch.
Reduce the amount of nanosecond gain.
Use PS OPCPA
  Limited ASE window
  Double reflections won’t be amplified
Requires optically synchronised pump beam
No recompression or cleaning

## Slide 6
Single stage PS OPCPA
Ti:Sapphire
Seed
Regenerative
Amplifier
2w
BBO
Pulse Length Control
Timing Control
Common seed for signal and pump pulses-optically synchronised
Gain Narrowing in Nd:YLF amplifier increases pulses to ~10ps
Stretcher in signal beam enables pulse length matching
500J
1mm
15mm

## Slide 7: PS OPCPA Performance
Demonstrated full amplification of seed laser at > 20nm
SSG~106 at peak of pump
120μJ for <1nJ input ~ 40% conversion of pump to signal and idler
Operates in a saturated regime
Measured RMS pulse to pulse stability ~1%

## Slide 8: High and Low Energy Seed operation of the ns OPCPA
Output | SSG | SSG | SSG | Input
10mJ | 102 | 103 | 103 | <1nJ
15mJ | 102 | 103 | 0 | ~20μJ

## Slide 9: ASE contrast Measurements
Relayed a beam out of the interaction chamber
Used single-shot AC to confirm compression
Optics limit the energy to just the rod amplifier chain

## Slide 10: Ns Contrast Measurements
Used a combination of a water cell and diodes to obtain a dynamic range of ~1010
Scattering from collimating optic used as timing marker.

## Slide 11: Contrast Measurement of the CPA and OPCPA systems
  Pick Off beam at injection to rod chain
  Relay and expand beam before injecting into the TAP compressor

## Slide 12: Sequoia Measurements
Using same beam line as the diode traces
Running both OPCPAs but no rods or disks

## Slide 13: Fluorescence from the Pump
FT of Clipped spectrum in stretcher gives steep gradient for contrast
Pump pulse varies in time.
SSG and therefore the PF will vary with the pump pulse intensity

## Slide 14
CPA beam
Long pulse
RCF stack
Reflected energy monitor
Optical probe
2x HOPG
2-D Ka imaging
X-ray multi-pinhole camera
Same energy on target in all cases
First Experimental Data
Courtesy of P.McKenna

## Slide 15: Conclusions
Original ASE Contrast
New ASE Contrast
Demonstrated a ps OPCPA that has improved the ns ASE contrast by at least 2 orders of magnitude.
Characterised the close in contrast.
Successfully delivered for user experiments