## Slide 1
Efficient scaling of output pulse energy in static hollow fiber compressors
X. Chen, A. Malvache, A. Ricci, A. Jullien, R. Lopez-Martens
ICUIL 2010, Watkins Glenn, 29 september 2010
http://loa.ensta.fr/
UMR 7639

## Slide 2
Size of focus
~ 2
“lambda cube” regime
Wavefront correction
Goal: relativistic intensity at 1kHz
Peak intensity
~ 1019 W/cm2
Deformable
Mirror
Target
Low f
parabaloid
Tight focusing
1 mJ, 5 fs 1 kHz
Albert et al., Optics Letters 2000

## Slide 3
Hollow fiber compression principle
  Spectral broadening via SPM in rare gas
  Guided propagation
  High damage threshold, low absorption
  Compression using chirped mirrors
standard: 25fs ~ 1mJ
< 10fs < mJ
Scaling limited by ionization/self-focusing
Nisoli et al., Appl. Phys. Lett. 68, 2793 (1996)

## Slide 4
Solutions
  Pressure gradients (5m, 5fs)
  Bohman et al., Opt. Lett. 35, 1887 (2010)
  High pressures, large setups
  planar waveguides (8mJ, 11fs)
  Akturk et al., Opt. Lett. 34, 838 (2005)
  complex setup, non-uniform beam
  guided ionization (12fs, 14 mJ)
    Fourcade Dutin et al., Opt. Lett. 35, 253 (2010)
    Blue-shifting, high losses

## Slide 5
Circular polarization
n2 (CP) = 2/3 n2 (LP)
Less self-focusing
Better coupling
Into fiber
Reduced ionization
Experimental
conditions

## Slide 6
Commercial Front-end
Femtopower Compact Pro CEP
Single pump laser
11 W
1 kHz frequency-doubled Nd-YLF laser
DM50 series Photonics Industries
Home made
3-pass amplifier
20 W
CEP-stable multi-mJ laser
Hybrid compressor:
Transmission gratings +
chirped mirrors
2 mJ, 26 fs, CEP stabilized pulses
Canova et al., Opt. Lett. 34, 1333 (2009)

## Slide 7
High energy hollow fiber compression
Chen et al., Opt. Lett. 34, 1588 (2009)

## Slide 8
Circular polarization = higher throughput
  better coupling
  up to 30% more transmission

## Slide 9
More stable propagation for CP
CP = more stable propagation
LP
CP
Spectral stability

## Slide 10
1mJ, sub-5fs, CEP locked pulses
Sub-5fs duration
Robust CEP lock (~250mrad)

## Slide 11
Commercial Front-end
Femtopower Compact Pro CEP
Single pump laser
11 W
1 kHz frequency-doubled Nd-YLF laser
DM50 series Photonics Industries
Home made
3-pass amplifier
20 W
Laser upgrade
Hybrid compressor:
New transmission gratings +
chirped mirrors
2 mJ, 26 fs, CEP stabilized pulses
3.5 mJ, 26 fs, CEP stabilized pulses

## Slide 12
Pulse pre-chirping in Neon
  3 mJ input
  70 %
  < 27 %

## Slide 13
Controlled spectral broadening

## Slide 14
Optimal results
1.6 mJ, sub-5fs
(after chirped mirrors)
CEP control

## Slide 15
On-target intensity
1.6mJ, 4.8fs
target
f/1.7 parabola
Beam expander
Vacuum chamber
HHG
1.7 x 1.8 mm2
Imax ~ 3 x 1018 W/cm2

## Slide 16
Confirmed by solid target HHG results
f/6 focusing : 3 x 1017 W/cm2
HHG spectra
CEP dependence
9 10 11 12 13
Harmonic order
100
200
300
CEP (deg)

## Slide 17
Further scaling options
  Higher energies: Helium gas

## Slide 18
  more efficient chirped mirrors
  Ultrafast Innovations GmbH (Pervak et al., Opt. Exp. 17, 7943 (2009))
Further scaling options
1.9mJ, 4.3 fs (63% !)
Raw FROG trace
Temporal profile
Better compression in UV
Need to work on IR

## Slide 19
  circular polarization
  Helium gas
  input pulse pre-chirping
  larger core fiber (~ 400 mm)
  CEP-stable, 5mJ, 5fs (1 TW)
  « compact » setup
  Imax 1019 W/cm2
Future with laser upgrade to 10mJ: