## Slide 1: Progress of the Fast Ignition Drive Optics upgrade to the ARC beamline on NIF
ICUIL 2010 September 30, 2010
Doug Homoelle, M. Rushford, N. Wong, P. K. Patel,
M. H. Key, A. Kemp, L. Divol, T. Schindler, K. McCandless, C. Widmayer, S. Fochs, J. Heebner, T. Budge, M. Bowers

## Slide 2: Fast Ignition Drive Optics (FIDO)
X (µm)
X (µm)
2
FIDO is a planned upgrade to the ARC beamline to enable/optimize high-intensity, high-energy density experiments on NIF
FIDO Missions:
  Improve beam quality
  Improve beam pointing
  Phase split-beam apertures
ARC Near-Field
ARC Quad Performance with FIDO: Far-Field
Expected ARC Quad Performance: Far-Field
cone tip
cone tip
X (µm)
X (µm)

## Slide 3: Fast Ignition Coupling Science Experiment & ARC Requirements
The Fast Ignition coupling experiment has set the current requirements for FIDO
ARC laser parameter | FI ARC requirements | Current ARC capabilities | Required improvement
Energy in 40 μm diameter | ~3-4 kJ | < 280 J | >15x
Intensity at the cone tip | 1020 W/cm2 | ~1018 W/cm2 | 100x
Pulse Length | 5-10 ps | 1-50 ps | 
ASE energy relative to main-pulse energy | < 10-6 (10 mJ) | < 10-4 (60 mJ) | 
Intensity contrast 100 ps before main pulse | < 10-6 | < 10-6 | 
Beam pointing error relative to cone tip (rms) | +/- 10 μm | +/- 75 μm | 7x
ARC to NIF timing jitter (rms) | +/- 40 ps | +/- 6 ps | 
To meet the fast ignition requirements, the residual wavefront error must be < l/10,
pointing error <1.1 mrad

## Slide 4: FIDO Architecture (simplified)
FIDO will be an adaptive optics system that makes use of a point source at the target to measure aberrations in the NIF laser
System design has been described in detail elsewhere:
  ICUIL 2008, C. W. Siders et al.
  IFSA 2009, D. Homoelle et al., J. Phys: Conf. Ser., 244, 032007 (2010)
  K. L. Baker et al., Opt. Expr., 17, 16696 (2009)
Basic principle of operation:
AO
System
Amp
Amp
Amp
3) Propagate NIF Laser
1) Fire point source, phase accumulates during
back-propagation through laser chain
2) Measure phase, set DM to appropriate shape

## Slide 5: FIDO Architecture Limitations
Proposed system is designed to operate at 1 kHz, but bandwidth of system vibrations and aberrations have not been determined
  We have undertaken a measurement campaign on NIF to quantify these effects and set bandwidth requirement for FIDO system
Method will work perfectly if all the aberrations are present and static during a correction cycle, but what if all aberrations are not present?
  The largest-amplitude aberration comes from laser slab heating after flashlamps are fired, ~400msec before shot
    Aberration is fully present <10msec before shot
    No current AO hardware can operate this quickly
    This issue is addressed through system modeling

## Slide 6: Sources of ARC Aberration and Jitter
Any beam correction system must account for all the system aberrations and jitter, both in magnitude and frequency
Target Motion:
Jitter: TBD mrad, <100Hz
Amplifiers:
Residual Jitter & WFE: TBD
Timescale: <300msec
Preamp:
Jitter: 0.5 mrad
WFE: l/20
Timescale: <500msec
Transport Optics:
Jitter & WFE TBD
Transport Optics:
Jitter: < 9mrad, <100Hz
WFE: (l/150)/cm per optic
  l/3 P-V, 0.3l power removed
  13 Optics
Beam Path Atmosphere:
Jitter & WFE: ~1Hz
Compressor Assembly:
Affects Phasing between beams
Non-common Path Errrors
Jitter & WFE: TBD
RP9: Proposed Location for AO System

## Slide 7: Front-end Jitter Measurements
Jitter from the front-end, before RP9, will be transferred to the beam with the current FIDO design
Front-end
X-axis
Y-axis
5-mrad total jitter, 1.5 mrad of high-frequency (>10 Hz)
  After beam expansion, reduced by 12.5x
High-frequency components at ~55 Hz and ~120 Hz
  Traced to cooling fans in electronics rack
Unless fixed, half of pointing budget consumed here

## Slide 8: Jitter measurement: ISP to OSP (B353)
Jitter measurement from the Preamp, 4 passes through the Main Amp, 2 passes through Power Amp, to the Transport Spatial Filter
X-axis
Y-axis
0.9-mrad total x-axis jitter, 0.6 mrad of high-frequency (>10 Hz)
  X-axis is vertical in the NIF beam
Unknown source, but frequency should not be challenging for a 1-KHz system

## Slide 9: Planned jitter measurement: 3w OSP to Target Chamber Center
Measurement has been delayed due to high-priority Ignition-related experiments in the target chamber
  Will characterize vibrations in remaining transport optics and target vibration

## Slide 10: Sources of wavefront error
Static aberrations in manufactured optics
  Mirrors, lenses, laser slabs
  Measured before installation on NIF
Turbulence in the beamline atmosphere
  Residual heat from previous shots, changing building temperature, tour lights, etc.
Prompt aberration from flashlamp heating of the laser slabs in the Multipass Amp (MPA), Main Amp (MA) and Power Amp (PA)
  Time scale < 500 msec

## Slide 11: Atmosphere-induced aberrations
Wavefront data of ISP-OSP path at 15-Hz with OSP wavefront sensor for 1 minute
B351 Pixel:
X = -0.77 mm Y = -0.67 mm
Single Pixel Data

## Slide 12: Turbulence Dynamics
We wish to determine the time period over which the turbulence aberration may be considered static
Take difference in wavefront values DWF for different times Dt between frames
Average of this difference + 3*std dev: 99% of time DWF will be less than this value
DWF <l/50 for Dt < 0.1 sec
3s Wavefront Variation
20x20 Central Pixels
Reminder: FIDO requirement is WFE < l/10

## Slide 13: Prompt Aberrations
Prompt aberrations are induced by the heat deposited to the laser slabs when the flashlamps are fired <500 msec before shot
  Occur in both the MA and PA and the MPA
  Expected that full aberration present < 10 msec before shot
No adaptive optics hardware can operate this quickly
If prompt aberration is repeatable (DWF<<l/10), we could possibly apply a static offset to correct for it
Experiment: Measure repeatability of prompt-only aberration on NIF by firing 2 pulses 100 msec apart
  First pulse fired 100 ms before main system shot
    used to measure all the static aberrations up to OSP
    atmosphere is “static” on this time scale
    pulse experiences no gain
  Second pulse fired to coincide with peak of gain curve
    used to measure all the static aberrations plus the prompt aberration at the peak of the gain curve
  The difference in the measured wavefronts yields prompt-only aberration

## Slide 14: NIF Prompt Aberration Experiment
Many changes must be made to the standard NIF operating procedure to make this happen
  Regen laser must be double-pulsed
    special triggering required for laser diode and Pockel’s Cells
  Main amplifier must be aligned in two-pass mode
    PEPC will not allow two pulses 100 ms apart through the system in 4-pass mode
  Must have special data collection hardware and software to acquire wavefront images at maximum rate
  Must have a specially tailored pulse to balance energy of the two pulses at the wavefront sensor
100 ms
MA/PA Gain Curve
Regen
Double-pulse timing with NIF Gain Curve
MOR Pulse Shape
t (ns)
Amplified pulse

## Slide 15: Repeatability of MPA Prompt aberration
Experiment on NIF has been delayed because of higher-priority ignition shots
We have executed the same experiment on the pre-amplifier module (PAM) to measure the prompt aberration in the MPA rod
  Different WFS required 200ms between pulses
  Different gain required slight mis-timing from peak of the gain curve
  14 pairs of wavefront data
Mean Prompt-only Aberration
St. Dev. Prompt-only Aberration
Prompt MPA aberration repeatable
to < l/30 for much of the beam

## Slide 16: FIDO Modeling
Model FIDO system using two techniques
  FRED, non-sequential raytrace using complex raytracing
  PROP, LLNL-written wave-optics propagation
FIDO operation modeled as follows:
  Determine shape for NIF DM to correct only for prompt aberrations
  Back-propagate light through laser system with all static aberrations present, prompt aberration not present, and DM with prefigure from step 1
  Measure phase at RP9, subtract contribution of DM to phase
  Forward propagate from RP9 through laser with both static and prompt aberrations present, DM set to prefigure
  Calculate phase variance at the output of the laser chain

## Slide 17: FIDO Challenges
If prompt aberrations are highly repeatable, how well will the FIDO system operate?
Challenge:
  Not measuring wavefront when all aberrations are present
    outgoing waves will go through path slightly different from measured path when prompt aberrations are present
Static Aberrations
Prompt Aberrations
TCC
FIDO

## Slide 18: FRED Modeling Results, no FIDO
Calculated phase at RP16 (right before injection into compressor) without FIDO correction, “perfect” DM pre-figure
Phase, Tilts Removed
Tilts & Focus Removed
~l/2 P-V

## Slide 19: FRED Modeling Results, with FIDO
Phase measured at RP16 (right before injection into compressor) with FIDO correction, “perfect” DM pre-figure
Phase
X-Lineout
Y-Lineout
Residual Phase Variance < l/20 for most of the beam

## Slide 20: Future Work
Finish beam jitter characterization: OSP to Target Chamber
Measure repeatability of prompt aberration in the MA and PA
Continue refining optical model:
  Use more realistic DM shapes
  Add spatial filters
  Include ARC-specific optics, compressor
A go/no-go decision will be made based on results of MA/PA measurement and modeling
  If go:
    Begin optical and mechanical design for ARC beamline
    Acquire appropriate hardware (DM, WFS), test & field
  If no-go:
    Think harder, think different

## Slide 21: Acknowledgements
Modeling Support
  Mike Rushford
  Nan Wong
  Kathleen McCandless
  Kai LaFortune
  Clay Widermayer
  Mike Shaw
Data Collection
  Tracy Budge
  John Heebner
  Tania Schindler
  Daren Hart
  Scott Fochs
  Erlan Bliss
Systems Engineering
  John Crane
Management
  Mark Bowers
  Chris Haynam
  Mark Hermann
NIF Wavefront Support
  Thad Salmon
  Steve Sutton
  Ron House
FI Support
  Prav Patel
  Mike Key
  Andreas Kemp
  Laurent Divol